## Slide 1
EMBEDDED VISION SYSTEMS · TECHNICAL BRIEF
Analyzing Real-Time Acquisition Constraints
in Embedded Vision Systems
A structured analysis using system-level timing, bandwidth, and pipeline models
Sensor Interface · Pipeline Timing · Bandwidth Modeling · Design Trade-offs

## Slide 2
Why Acquisition Timing Is the First Constraint
Embedded vision systems must capture, move, and process image data before the physical process outpaces them
Autonomous Platforms
Missed frames translate directly into blind intervals for obstacle and lane detection at speed.
Industrial Inspection
Line speed fixes the acquisition window; a late frame means a missed defect on a moving part.
Robotics & Drones
Closed-loop control needs bounded, predictable frame latency, not just a high average frame rate.
Surveillance & Safety
Event detection depends on sustained throughput without dropped or jittered frames over long runs.
Real-Time Acquisition Constraints in Embedded Vision Systems
2

## Slide 3
A System Model of the Acquisition Path
Every stage adds delay and consumes a shared bus — the model must capture both
Image Sensor
Exposure +
row readout
ISP / Front-End
Demosaic,
gain, format
Interconnect / DMA
MIPI, PCIe,
AXI bus transfer
Frame Buffer
DDR / SRAM
storage
Vision Processor
CPU / GPU / NPU
inference
System-level constraint: each stage has a service time and a buffer depth. The model treats the path as a queue chain — an increase in any stage’s latency or a stall in the interconnect propagates downstream and can violate the frame deadline before processing even begins.
Real-Time Acquisition Constraints in Embedded Vision Systems
3

## Slide 4
Four Classes of Real-Time Constraint
Structured explanation requires separating what is bounded from what is merely fast
Latency
Time from photon capture to a usable frame at the processing stage. Bounds reaction time in closed-loop systems.
Throughput
Sustained data rate the pipeline must move — sensor output bytes/sec must not exceed bus and memory bandwidth.
Jitter
Frame-to-frame variation in arrival time. Low average latency is meaningless if individual frames vary widely.
Determinism
Guarantee that worst-case timing, not just average timing, stays inside the deadline for every acquired frame.
Real-Time Acquisition Constraints in Embedded Vision Systems
4

## Slide 5
Modeling Frame Acquisition Time
The frame period is a sum of sequential, measurable component delays
Frame Period Model
T_frame = T_exp + T_read + T_xfer + T_proc
T_exp sensor exposure time T_read row-by-row readout time T_xfer interconnect transfer time T_proc processing / inference time
Real-time constraint: T_frame ≤ 1 / f_required
The pipeline is real-time only if the worst-case sum stays under the deadline set by the required frame rate — not the average case.
Timing Breakdown of One Frame Period
T_exp
T_read
T_xfer
T_proc
T_frame (must fit inside 1 / f_required)
Structured reading of the model
• Exposure and readout are sensor-fixed; they set a lower bound the rest of the system cannot recover from. • Transfer and processing are shared resources — contention here is where deadlines are usually missed.
Real-Time Acquisition Constraints in Embedded Vision Systems
5

## Slide 6
Bandwidth Grows Faster Than It Looks
Raw data rate D = Width × Height × bits-per-pixel × frame rate
Data-Rate Model
D = W × H × bpp × fps
W, H frame width / height (px) bpp bits encoded per pixel fps required frame rate D sustained bus load (bit/s)
Design rule: provisioned bus and memory bandwidth must exceed D with margin for refresh, arbitration, and burst overhead — not just match the average.
Sustained Bandwidth by Sensor Configuration (Mbit/s, 8bpp)
Chart: Mbit / s
| VGA 30fps | 720p 30fps | 1080p 30fps | 1080p 60fps | 4K 30fps
Required Bandwidth | 221 | 663 | 1493 | 2986 | 5972
Real-Time Acquisition Constraints in Embedded Vision Systems
6

## Slide 7
Worst-Case Pipeline Latency Analysis
Deadlines are set by the worst path through the pipeline, not the average one
Pipelined Stage Timing
Capture
0.62 ms
Transfer
0.28 ms
Pre-process
0.45 ms
Inference
0.90 ms
Post-process
0.20 ms
WCET_total = Σ WCET_stage = 2.45 ms → bounds max sustainable rate to ~408 fps per single stream lane
Buffering Absorbs
Stage-Rate Mismatch
• Double- or triple-buffer between capture and inference to decouple sensor jitter from compute jitter. • Buffer depth must cover the worst observed stage-time variance, not just the mean difference. • Excess buffering trades latency for stability — every added frame of buffer adds one frame period of delay.
Real-Time Acquisition Constraints in Embedded Vision Systems
7

## Slide 8
Platform Comparison Under the Same Model
Applying the model to three common embedded vision targets
Constraint | MCU + CMOS Sensor | SBC (GPU-assisted) | FPGA Front-End
Max sustained fps | 15–30 fps | 30–60 fps | 60–120 fps
Typical latency | 20–40 ms | 8–20 ms | <5 ms
Bus bandwidth headroom | Low | Moderate | High
Jitter behavior | High (RTOS-dependent) | Moderate (OS scheduling) | Very low (hardware clocked)
Determinism guarantee | Soft real-time | Soft real-time | Hard real-time
Power envelope | <1 W | 5–15 W | 3–10 W
Real-Time Acquisition Constraints in Embedded Vision Systems
8

## Slide 9
Resolution, Rate, and Power Pull in Different Directions
The acquisition model exposes trade-offs before they become field failures
Resolution ↑
Higher spatial detail increases D linearly and lengthens T_read and T_proc — pushes T_frame toward the deadline.
Frame Rate ↑
Higher fps tightens 1/f_required, shrinking the margin every downstream stage must fit inside.
Power Budget ↓
Lower power caps clock speed and parallelism, directly increasing T_proc and WCET.
Design principle:
No single axis can be optimized in isolation. The acquisition model is used to find the feasible region where T_frame stays under the deadline for the chosen resolution, rate, and power point — then the platform is picked to fit that region, per Slide 8.
Real-Time Acquisition Constraints in Embedded Vision Systems
9

## Slide 10
Key Takeaways
1
Treat acquisition as a queue chain: sensor, interconnect, and compute stages each add latency and share bandwidth.
2
Design against worst-case timing (WCET), not the average frame period — determinism is the binding constraint.
3
Compute required bandwidth explicitly with D = W × H × bpp × fps and provision margin above it.
4
Use buffering deliberately: it trades added latency for absorbed jitter between mismatched stage rates.
5
Resolution, frame rate, and power form one coupled trade-off space — fix two, and the model bounds the third.
Real-Time Acquisition Constraints in Embedded Vision Systems
10